## Slide 1: Flightstream training
Daniel Enriquez | Technical Support | 09/05/20204

## Slide 2: Training Outline
2
Fundamentals
User Interface
CAD
  Import, Repair
Mesh
  Import mesh, Topology
Physics
  Trailing edges, Wake termination, Actuators, Inlets
Solver
  Viscosity, Steady subsonic solver
Unsteady Solver + Motions
Plots
  Forces, Residuals
Toolboxes
Post - Processing
Scripting

## Slide 3: Training Objectives
Familiarize users with the fundamentals of FlightStream.
  CAD
  Mesh
  Physics
  Post-processing
  Scripting
This training should cover 80-90% of the use cases. However, there are unique capabilities available for edges cases (just ask!)
It is recommended you follow along using both the slides and by having FlightStream open during the presentation.
FlightStream can do a lot! It takes a few hours to get started, but several hundred hours to master.

## Slide 4: Training Legend
Italic titles = this is a practical hands-on example.
Key take-aways are in blue boxes!
 Stop signs denote “end of practical example”

## Slide 5: FlightStream Solver Fundamentals

## Slide 6: Potential Flow
FlightStream is based on inviscid potential flow. It solves the vorticity around the geometry by dividing the geometry into surface-panels of bound vorticity.
Vorticity is shed into the wake via trailing edges. This creates circulation which creates lift!
By solving for surface vorticity and induced velocity, integrated aerodynamic loads can be calculated.

## Slide 7: Viscous Effects
After the initial velocities and pressure are calculated, integral boundary layer methods are used to estimate boundary layer properties.
A second iteration virtually perturbs the geometry boundaries to capture the viscous effects on the inviscid flow field.
= boundary layer thickness
= displacement thickness
When troubleshooting, run the inviscid solution only since viscous corrections are a post-solution step

## Slide 8: Surface Mesh
The panel method found in FlightStream only requires a surface mesh to solve the flow field.
At solver time, an octree Cartesian field is constructed to calculate the volumetric flow properties.

## Slide 9: Potential Flow Limitations
While FlightStream does capture some viscous/separation effects, the models are tailored to external vehicle aerodynamics. Here is list of flow which is not resolved by FlightStream:
  Highly separated/swirling bulk flow.
  Highly transient/dynamic separation.
  Flow within small gaps
  Viscous-dominated flow such as that found in shear layers or rotating objects.

## Slide 10: Graphical user interface

## Slide 11: User Interface

## Slide 12: Scenes
There are 4 scenes:
  CAD - full surface representation CAD model.
  Mesh – unstructured mesh representation.
  Solver – solver contours and post processing.
  Plots – XY plots of various solver parameters.
If you can’t find your geometry, look at what scene you are in!

## Slide 13: User Interface - Toolbar
The toolbar offers a quick shortcut to many common FlightStream operations.
The best way to learn the tools is to click around and find out. Hover over them for tool tips.
File I/O
View shortcuts
Solver
Initialization
Mesh/Geometry Selection
Mesh Normals
Mesh Edge Editing Tools
Vertex Editing Tools

## Slide 14: User Interface - Statistics
Statistics show the mesh face/vertex count and the relative size of the geometry.
Check this window to make sure your model size is correct!

## Slide 15: User Interface – Control Menu
Simulation units can be changed here
Angle for detecting/selecting features.
Max angle for trailing edge detection.
Angle for selecting base regions.
Tolerance for agglomerating coincident vertex clusters into single vertices
1
2
3
4
5

## Slide 16: User Interface – Solver
Angle-of-Attack, Side-slip Angle: values vary between -89o and +89o. The default value is 0o.
Reference velocity, Reference length and Reference area are used to convert the forces and moments evaluated by FlightStream into dimensionless coefficients. The reference velocity is used in conjunction with the fluid density
Parallel threads allow computation speed up by using multiple CPUs
Minimum Cp: Minimum value allowable of Cp. Useful to stabilizing solutions.
Non-dimensionalization of moment example

## Slide 17: User Manual
Refer to the User Manual!
There is a lot of questions that can be answered here.

## Slide 18: CAD

## Slide 19: CAD - Basics
IGS
STL

## Slide 20: CAD - Basics
Users can utilize CAD to build Meshes in variety of ways.
In FlightStream, CAD can be:
  Imported from an IGS (only)
  Generated from basic shape primitives: Cylinder, box, o-give, sphere
  Constructed from cross section curves (CCS)
  Constructed from an existing mesh (STL)

## Slide 21: CAD - Manipulating
After creating/importing CAD, the user can scale, rotate, and translate geometry.
Splitting the geometry faces into components is best practice.
  For example, split wing faces, horizontal stabilizer, fuselages, etc.

## Slide 22: CAD - Tessellation
In the CAD window you can re-tesselate faces with either the aligned mesher or trimmed mesher.
Baseline mesh
Trimmed mesh
Aligned mesh
(unstructured)
(mapped edges)

## Slide 23: CAD – Trimmed Mesher
Trimmed mesher is an unstructured edge-size based mesh generator.
See User Manual for more details on these options.

## Slide 24: CAD – Aligned Mesher
The aligned mesher allows the user to created mapped meshes on quad face sheets.
The face directionality follows:
  Red
  Green
  Blue
  Cyan
You can specify node count and growth rate on each side.
1
2
3
4
Source
Target
Sweep 1
Sweep 2

## Slide 25: CAD – Curves
At the CAD level, geometry curves maintain their true geometric representation. In other words, they are independent of CAD tessellation.

## Slide 26: CAD – Box Example
We’ll start our exploration by creating and meshing a box.
1
2
3
Right click CAD>New
Right click CAD Model>Create
Create a new cube

## Slide 27: CAD – Box Example
4
Enable face selection in toolbar
5
Select a face, and retessellate it
With the trimmed mesher
*Toggle the wireframe to show mesh
6
7

## Slide 28: CAD – NASA CRM Example
Let’s import the NASA CRM – IGS file
1
2
*Leave defaults

## Slide 29: CAD – NASA CRM Example
Now we’ll remesh a face using the aligned mesher
3
Click the green cube to show the normal
Green shading is normal pointing outward.
Red is normal pointing in.
Select the face, right click
Retessellate > Aligned mesher
Remap the aligned mesher nodes to look like this. You will need to change the source and target distributions to 10/10
Right click the node to change the color.
Toggle the mesh
4
5

## Slide 30: CAD – Extracting Cross Sections Example
Now let’s extract cross sections from the wing, to build our CCS file

## Slide 31: CAD – Extracting Cross Sections Example

## Slide 32: CAD – Extracting Cross Sections Example

## Slide 33: CAD – Extracting Cross Sections Example

## Slide 34: Challenge
Open the User Manual
Add Parameters to the CCS file:
  Mark_trailing_edges
  Blend_trailing_edges

## Slide 35: Mesh

## Slide 36: Mesh - Basics
In FlightStream, the mesh is used to calculate the flow field solution.
Breaking up the model into various components can aid in troubleshooting, in generating aerodynamic loads, and in post-processing the solution.
Break your model up into components!

## Slide 37: Geometry Workflow
Geometry typically comes in the form of analytical IGS or a mesh file type such as STL/OBJ
Various meshing tools within FlightStream allow for the creation of a final analysis-ready mesh

## Slide 38: Mesh - Importing
Meshes can be imported in a variety of formats: STL, TRI, AC, OBJ, P3D, CCS
P3D is the recommended mesh format for importing since it maintains underlying quad representation. FlightStream can perform mesh agglomeration (during initialization) and convert triangles to quads to reduce mesh count!
  OpenVSP can easily export P3D
Baseline Mesh
Agglomerated Mesh

## Slide 39: Mesh – Tools
Split Edges
Swap Edges

## Slide 40: Mesh – Tools
3. Connect Edges (commonly used)
4. Hole Fill (commonly used)

## Slide 41: Mesh – Tools
5. Select Edges By Path (commonly used)
6. Smooth Vertices

## Slide 42: Mesh – Topology Window
The topology menu has several tools for diagnosing and improving the mesh.
Diagnostics
Mesh Tools

## Slide 43: Mesh – Topology Diagnostics
All red values should be 0 to prevent solver divergence.
Free edges are ok, if they are intended. For ex., when using mirror boundary conditions.
Orange/yellow boxes are ok if intended. (But rarely happen)

## Slide 44: Mesh – (Common) Topology Fixes
Degenerate faces can simply be deleted. Click the red box and then delete.
Inverted faces need the surface normal flipped. Select the face and invert.

## Slide 45: Mesh - Component Cross Section (CCS)
Component Cross Section format is the most versatile way to create meshes in FlightStream.
With only cross section definition, many components can be created.
CCS file rows for building a wing

## Slide 46: Mesh - Component Cross Section (CCS)
Example CCS components
Fuselages
Nacelles & Annular Ducts
Wings with Control Surfaces

## Slide 47: Mesh - Component Cross Section (CCS)
Parameters in the CCS file allow you to control meshing and geometry.
Subsurface;Name;v0;v1;u0;u1;hinge_height;rotation_angle;slot_gap_percentage
MorphCS;Name;v0;v1;u0;u1
Parameter;Blunt_trailing_edges
Parameter;Blend_trailing_edges
Mesh_U;u_pts;growth_type;growth_rate;periodicity
Some Parameter Examples
See the User Manual for more details!

## Slide 48: Mesh – Wing STL Example
Now let’s say you have an STL file, how can we convert this into a CCS?

## Slide 49: Mesh – Wing STL Example

## Slide 50: Mesh – Wing STL Example

## Slide 51: Mesh – Wing STL Example

## Slide 52: Mesh – CCS Wing Example
Try to add a control surface to the sample ccs file

## Slide 53: Mesh – CCS Wing Example

## Slide 54: Mesh - OpenVSP
FlightStream has been engineered to “play nice” with OpenVSP.
OpenVSP is an aircraft geometry drafting software.
Meshes from OpenVSP can be directly used in FlightStream. Use P3D file format for best results.

## Slide 55: Mesh – OpenVSP Example

## Slide 56: Mesh – OpenVSP Example

## Slide 57: Mesh – OpenVSP Example
We have imported the mesh, but it is not watertight. We need to unite the model to do this.

## Slide 58: Mesh – OpenVSP Example
You now have a watertight mesh (almost) ready for analysis.
Save this .fsm file for later use.
FlightStream automatically takes care of the wing-fuselage intersections!

## Slide 59: User Feature Edges
Feature curves can be helpful in defining new features in the model that are not part of the existing components.
Example of creating features

## Slide 60: Physics setup

## Slide 61: Physics
At its core, FlightStream is a potential inviscid solver.
However, there are several models that have been developed to enhance the baseline physics. These include:
  Viscous corrections (Boundary layer methods)
  Flow separation models
  Compressibility corrections (Sub-, Tran-, *Super-, *Hyper-)
  Time-accurate solver

## Slide 62: Trailing Edges
All lifting components need to have trailing edges defined.
Intersections with non-lifting bodies need to have wake termination nodes defined.
Trailing edges
Termination
nodes
Menu for selecting TE and Nodes

## Slide 63: Base Flow Regions
Areas of separated bulk flow for example behind fuselages or wing blunt trailing edges.
Base regions apply a constant Cp on these faces.

## Slide 64: Viscous Corrections
FlightStream uses integral boundary layer methods to calculate boundary layers from surface pressures.
These viscous corrections affect the forces and moments on the body by virtually deflecting the surface boundary.

## Slide 65: Flow Separation
“Stratford” separation models are used for bodies and wings. Model is based on detection of adverse pressure gradients.
  Axial separation: wings + fins. Flow is primarily axial along the wing.
  Crossflow separation: for low AR bodies like fuselages.
Separation contours on an aircraft

## Slide 66: Freestream Fluid
Freestream settings can be set under the “Fluid” node

## Slide 67: Physics – Airliner Example
Let’s run our first solution
Open the previously saved .fsm file

## Slide 68: Physics – Airliner Example

## Slide 69: Physics – Airliner Example
Bonus: try to initialize only parts of the aircraft.
Initializing + running only subcomponents is useful for troubleshooting your case.

## Slide 70: Additional Physics – Actuators
Actuators – Simulate pressure/density change in volume.
  Propeller model – Adds thrust, swirl, and induced velocity to the flow
  Exhaust model – Adds thrust, and induced velocity to the flow

## Slide 71: Physics – Airliner Example
Now let’s add a propeller and jet exhaust to the airliner

## Slide 72: Physics – Airliner Example

## Slide 73: Physics – Airliner Example

## Slide 74: Physics – Solver Divergence
How to identify solver divergence?
  Vorticity ‘blows up’
  Residuals increase
  Nonsense aerodynamic loads

## Slide 75: Physics – Analysis Tab
Refresh –
After running, must refresh loads
Copy/export table –
For further analysis in spreadsheet format
Export solver data –
Surface solution to VTK format

## Slide 76: Physics – Analysis Tab
Under Units can change the units used for force/moment calculations.
The options set in the Analysis tab will be used for loads in Solver Sweeper toolbox!

## Slide 77: Physics – Analysis Tab
Breakdown of forces/moments by component is available.
This table is useful for troubleshooting; check relative forces of components

## Slide 78: solver

## Slide 79: Solver
The Solver scene is where you visualize the on-going solution.
In this scene you can visualize any items created under Post-Processing in the simulation tree.

## Slide 80: Solver – Scene Settings
Options for what to show in Solver scene can be toggled under the gear icon.

## Slide 81: Solver - Toolbar
Initialize the case
Run the case
Clear Solution
Clear Initialization

## Slide 82: Solver - Initialization
Select solver model
Controls the maximum level of stabilization to be applied to maintain convergence
Select the appropriate symmetry boundary conditions
Detection and stabilization between geometry components in close proximity of each other (for example, between a stowed control surface or flap and the wing)
Specify the downstream termination location of the wake strands
Enable the wake collision avoidance model that prevents wake strands from intersecting boundary faces

## Slide 83: Solver - Initialization
Custom size level of the wake Cartesian grid used for propagation of wake filaments
Specify the boundaries where triangle-pairs should be converted to quads in the solver
Select the surfaces that need to be added to the solver
Treat all moving mesh boundaries in the unsteady solver as acoustic sources
Starts the solver initialization

## Slide 84: Compressible Flow
New in 2024.1: Menu for selecting different compressibility solvers.
Incompressible: – Standard incompressible solver
Subsonic: – Incompressible solver w/ compressibility correction
Transonic: – Non-linear transonic field-panel solver
*Supersonic: – Linear supersonic panel solver (*Exp. release in 2024.2)
Hypersonic: Ma->5

## Slide 85: Solver - Contours
Right clicking in the scene window allows users to change contour variable.
Flow parameters variables can be shown.
Viscous variables can be shown.

## Slide 86: Plots

## Slide 87: Plots
The Plots scene shows XY plots from various sources in FlightStream.

## Slide 88: Plots – Iterations
Can view Residuals and Forces. These are helpful for viewing solution convergence

## Slide 89: Plots – Sectional Forces
Can view automatically created Sectional lift forces.

## Slide 90: Plots – Section Pressure
Can view pressure distributions over user defined Cross Sections.

## Slide 91: Plots – Solver Sweeper
The results from the Solver Sweeper toolbox can be plotted to show forces vs sweep variables for example: vs

## Slide 92: Toolboxes

## Slide 93: Toolboxes
Currently there are 4 toolboxes in FlightStream (more in development)
Two are commonly used:
  Solver Sweeper
  Stability & Control

## Slide 94: Toolbox – Solver Sweeper
The most commonly used tool is solver sweeper.
It allows you to sweep various solver parameters to generate aerodynamic databases.
Sweep parameters
Export file window
Force/moment results

## Slide 95: Toolbox – Stability & Control (SCT)
Allows you to setup Stability & Control derivatives
FlightStream automatically perturbs the solution file to calculate the desired derivatives.

## Slide 96: Physics – Airliner Example – Solver Sweep
Open the previously saved fsm file.

## Slide 97: Physics – Airliner Example – Solver Sweep

## Slide 98: Physics – Airliner Example – Stability Toolbox

## Slide 99: Unsteady solver

## Slide 100: Unsteady Solver
Unsteady solver is useful for analyzing time dependent motions in FlightStream

## Slide 101: Unsteady Solver – Solver Setup
Time increment: between time steps
Time-stepping iteration: how many total time steps to solve
Plots: Unsteady solver plots such as forces/moments
Right click on Solver to change the solver type

## Slide 102: Unsteady Solver – Plots
Allow you to monitor
  forces/moments
  Point fluid values
  create animations
During solver execution

## Slide 103: Unsteady Solver - Motions
There are 6 types of motions:
  Euclidean – basic translation/rotation given velocity/acceleration
  Custom – user defined motion profile with either position or velocity
  6DOF – aerodynamic forces applied to an inertial body
  Fluid-Structure Interaction – aerodynamic forces applied to a flexible structure
  Flight Control System – Apply time varying control deflections to specify maneuvers
  Atmospheric Gust – Apply gust profiles to simulation
Euclidean and Custom are the most commonly used.

## Slide 104: Unsteady Solver - Rotor
First we will create the rotor geometry

## Slide 105: Unsteady Solver - Rotor

## Slide 106: Unsteady Solver - Rotor

## Slide 107: Unsteady Solver - Rotor

## Slide 108: Unsteady Solver - Rotor

## Slide 109: Unsteady Solver - Rotor

## Slide 110: Unsteady Solver - Rotor
We will setup the rotor to run at 1800 RPM (188.5 rad/sec)
Time step should be set such that ~8-10 degrees are swept in one time step for a total of 3 revolutions.

## Slide 111: Unsteady Solver - Rotor

## Slide 112: Unsteady Solver - Rotor
Initialize
And then run the solver
Save the fsm file

## Slide 113: Unsteady Solver - Rotor
This plot needs updating

## Slide 114: Unsteady Solver – Custom Motions
In the same file, we’ll create a new custom motion

## Slide 115: Unsteady Solver – Custom Motions

## Slide 116: Unsteady Solver – Custom Motions
The new csys and the rotor fly away from the origin!

## Slide 117: Troubleshooting

## Slide 118: Troubleshooting
Review the mesh.
  Look in the Topology tab. See if there are any holes or degenerate faces in the mesh and address those first.
  Ensure you have a watertight geometry. Apply Unite!
  Ensure the model is scaled appropriately. See the Statistics tab.
Review boundary conditions
  Ensure all surfaces are assigned with correct physics models.
  Review trailing edge and wake termination assignment. Often, incorrect specification can cause solver divergence.

## Slide 119: Troubleshooting
Review the Solver Settings. Incorrect values can cause divergence.
Initialize and Run one boundary at a time to find which one is causing divergence.
Review Initialization setup

## Slide 120: Post-processing

## Slide 121: Post-Processing
FlightStream has several tools for post-processing and analyzing your solution.
  Probe Points: Extract flow parameters at specific (x,y,z) points in the field
  Surface Sections: Extract flow parameters on the geometry. Ex. surface pressure distributions & sectional loads.
  Volume Sections: Visualize flow parameters in the volume.
  Off-body Streamlines: Generate streamlines in the flow field.
  On-body Streamlines: Generate streamlines on the surface of bodies.
  Export VTK: Export solution for use in another post-processing software, ex. Tecplot or Paraview.

## Slide 122: Post-Processing - Probe Points
User can create probes interactively
Or import them from a text file
Or generate them on surfaces, selected vertices, or line surveys.

## Slide 123: Post-Processing – Surface Sections
User can create single surface sections or distributions.
Component sectional loads can be generated with this tool.

## Slide 124: Post-Processing – Volume Sections
User can create volume sections to visualize the flow field.
These volumes can be exported as VTK.

## Slide 125: Post-Processing – Off-body Streamlines
Off-body streamlines can be created to visualize the flow field

## Slide 126: Post-Processing – On-body Streamlines
On-body streamlines can be created to visualize the flow field
  Click on New Surface Streamline, then a vertex on the body to generate

## Slide 127: Post-Processing - Colormap
Colormap options can be changed

## Slide 128: Post Processing - Practice
Use the various post processing tools to visualize the flow around the Commercial Airliner example

## Slide 129: scripting

## Slide 130: Scripting
FlightStream allows users to script the execution of any simulation in order to automate the entire process.
Scripted commands are provided to FlightStream via a text-based script file.
Comment block 
Commands 
FlightStream is sensitive to line spacing and exact appearance of commands. Always ensure you follow the User Manual!

## Slide 131: Scripting - Example
Write a script to open the
  Open the fsm file : 777.fsm
  Set the solver settings
  Initialize the solution
  Run the solution.
Open the User Manual and copy and paste the needed commands

## Slide 132: Scripting - Example

## Slide 133: Scripting - Example

## Slide 134: Training Conclusion
We have covered 80-90% of the functionalities in FlightStream.
Cases will come up that require ‘hacking’. For support please contact us and we are happy to help
  Daniel.Enriquez@researchinflight.com
  Vivek.Ahuja@reseasearchinflight.com
We look forward to continued learning and collaboration!

## Slide 135: Challenge Problems

## Slide 136: Challenge 1 - Wing
Create a simple wing model in OpenVSP
Import p3d into FlightStream
Extract cross sections at the root and tip and create a CCS file.
Analyze the wing from the CCS file.

## Slide 137: Challenge 2 -Scripting
Set up a script that opens an fsm file and calculates the stability & control derivatives for various angles of attack.
  Setup your derivatives in the fsm file
  Write the script to open, initialize, and run the SCT

## Slide 138: Challenge 3 – Pitching Aircraft
Using the Commercial Airliner setup Unsteady Motions.
Use a Euclidean motion to pitch the aircraft up at a specified rate.
Now use a Custom motion to change the pitch angle of the aircraft.
  Hint: first create a text file with the motions.